## Slide 1: Introduction to IPv6
Kurt Erik Lindqvist
Kurtis@kurtis.pp.se

## Slide 2: Agenda
Background of IPv6
IPv6 Design and addressing
Routing
Transition from IPv4 to IPv6
IPv6 and DNS
Applications
Is this good?

## Slide 3: Before we start…
+++++++++++++++++++++++++++++++++++
| Prefix (24 bitar) | |
+++++++++++++++++++++++++++++++++++
CIDR = Classless Inter Domain Routing
Anything else on IPv4 and routing?

## Slide 4: Background of IPv6

## Slide 5: Background of IPv6
The original IPv4 addresses was not not CIDR.
In other words, the size of the address blocks where divided into classes; A (/8), B (/16) and C (/24) - which would correspond to different users needs.
  The blocks was originally handed out arbitrarily - especially in the ”B” category.
  In the early 90s this lead to serious concern that we would run out of addresses.
Notes: Stora delar av /8 delades ut till stora företag som IBM, HP, BBN etc
/16 delades ut godtyckligt och ofta
Oron basead på trend analys av IP adress utdelning.
Adress plan baserad på 1960-1970 talets planering.

## Slide 6: Background of IPv6

## Slide 8: Background of IPv6
A first step was to introduce CIDR
In other words, a assigned address block could have arbitrary prefix-length.
A parallel effort was started in 1992 to find a new addressing model for the Internet
  The first suggestion was based on ISOs OSI model
  Widespread resistance led to the suggestion being withdrawn.
Notes: CIDR krävde också ändringar till routingprotokoll.
Ändrat och laggt till _NY_ adressplan
Kritik av OSI
  Många ansåg att det hade en stor installed base
  Men hade många barn problem.

## Slide 9: Background of IPv6
In July 1992 the IETF decided that in order to move forward, a estimate of the future size of the Internet was needed.
  2020 : 10 Billon people
  100 computers per person
In order to give margin for poor utilisation and error, it was decided that we needed address space for
  10^15 hosts
  10^12 networks
Notes: Nyttjandegraden kring 1996 var 4% av tillgängliga adresser, tanken var att man skulle kunna fortsätta. Idag ligger vi runt 40-50%.

## Slide 10: Background of IPv6
Three proposals was made
  OSI
  IPv7: TP/IX by Robert Ullman
    Also wanted to change TCP
    Was compatible with IP, CLNP and IPX
  IP in IP: A mix of proposals, among others Steve Deerings SIP, PiP and IPAE
The IPng working group decided in June 1994 to use IP in IP as the base of the new protcol
  However, address size was increased to 128-bits
  The new proposal was called IPv6
Notes: Ip in IP hade 64 adresser och planen var att använda olika nät för global och lokal routng.
IPv5 var redan använt för streaming protokollet ST.

## Slide 11: IPv6 - current status
Notes: Asien / europa är drivande. Inget sikte av att 3G skulle driva detta så fort man trott, men mycket av utvecklingen sker där.

## Slide 12: IPv6 - current status

## Slide 13: Questions
How long will the IPv4 addresses last?
How will address policy be affected by 3G?
And by other “mass-applications?”