## Slide 1: IPV6 Design and addressing

## Slide 2: IPv6 Addressing
IETF decided for 128-bit addresses, instead of the classical 32-bits
IETF also decided to change a number of fields in the IPv6 header
Notes: - 128-bitar skulle svara mot den antagna tillväxten, antalet hosts och nyttjande graden
Man ville också försöka lösa en del problem man misslyckats med i IPv4
  Säkerhet
  QoS
  Flöden
  Robusthet

## Slide 3: IPv4 header
version
TOS
total length
fragment ID
0
fragment offset
source address
destination address
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
IHL
TTL
protocol
header checksum
(option line 1)
(option line 10)
DF
MF
Notes: Version = 4
IHL = Initial Header Length
TOS
Total length
Fragment ID

## Slide 4: IPv6 header
version
traffic class
flow label
payload length
next header
hop limit
source address
destination address
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
Notes: IPv6 header : 64-bitar + 2x128-bitars adresser’
----------------------------------------------------------------
Version 4 bitar
Priority value 4 bitar
Flow label 28 bitar
Length of payload 16 bitar
Type of next header 8 bitar
Hop limit 8 bitar
-----------------------------------------------
Endast versions fältet är samma och på samma plats.
Ursprungligen var meningen att varje IP stack skulle särskilja paketen baserat på versions fältet. Ändrades dock med att de särskiljs på media nivån. Tex i Eth 86DD=IPv6, 8000=IPv4.

## Slide 5: IPv6 Header - The big Headlines
All fields are of a predefined and static size
  Faster to process
  No “Initial Header Length” (IHL) needed.
  Instead a number of “extension headers” are defined
Header checksum is removed
  Speeds up processing av each packet as the checksum doesn’t have to be calculated.
  Packets can be incorrectly routed but the risk is to small
  The payload normally have it’s own checksum
Notes: Bortsett från Hop-by-hop behöver inte alla noder processa alla optional headers

## Slide 6: IPv6 packet - The News
Fragmenting is gone
  IPv6 will only send packet after Path Maximum Transmission Unit Discovery (PMTUD) is done
  IPv6 is missing the TOS field
Three fields will change name
  Packet length -> Payload length
  Protocol type -> Next header
  Time to live -> Hop Limit
Notes: PMTUD

## Slide 7: IPv6 extension headers
Hop-by-Hop
IPv6
Upper layer
Destination
Routing
Fragmentation
Authententication
Security
Destination
Processed by all nodes
Encryption / Decryption of the rest of the packet
Processed by all routers listed in ”routing”
List of routers that the packet needs to pass through
Processed by the destination
Processed after the original packet have been recreated
Processed by the destination
Notes: Ordnas i paketet i ordningen ovan. Betyder att noder / slutnod måste skala av dem i den ordningen.

## Slide 8: IPv6 extension headers
Extension headers is a list of headers
IPv6 Header
Next = TCP
IPv6 Header
Next = Routing
IPv6 Header
Next = Routing
TCP Header + Data
Routing Header
Next = TCP
TCP Header + Data
Routing Header
Next = Fragment
Fragment Header
Next = TCP
TCP Header
+ Data

## Slide 9: IPv6 extension headers
Next header-type coding is similar to the “payload-type” coding of IP4.
  Values are shared
Most are the same but there are several new ones
  0: Reserved (IPv4)/ Hop-by-Hop options (IPv6)
  1: ICMP (IPv4)
  2: IGMP (IPv4)
  3: ICMP (IPv6)
  59: No next header (IPv6)

## Slide 10: IPv6 extension header - Routing
Same function as source routing for IPv4
Next Header
Routing type=0
Segments left
Address[0]
Address[1]
0 8 16 24 31
Reserved
Header length
Notes: Next Header, identifierar följande header
Routing type, alltid 0. Framtida definitioner kan visa på andra typer av routing headers.
IPv4 kollade alla routrar om de fanns i source-route listan. I IPv6 kommer de bara att kolla det om de finns i destination adressen i headern.
-------------------------------------------
else {
decrement Segments Left by 1;
compute i, the index of the next address to be visited in
the address vector, by subtracting Segments Left from n
if Address [i] or the IPv6 Destination Address is multicast {
discard the packet
}
else {
swap the IPv6 Destination Address and Address[i]
if the IPv6 Hop Limit is less than or equal to 1 {
send an ICMP Time Exceeded -- Hop Limit Exceeded in
Transit message to the Source Address and discard the
packet
}
else {
decrement the Hop Limit by 1
resubmit the packet to the IPv6 module for transmission
to the new destination
}

## Slide 11: IPv6 extension headers - Fragmentation
Instead od doing fragmentation as in IPv4 by intermediary routers, IPv6 will trust PTMUD
Still an application might want to send a packet that is larger than the MTU
  The source host will then fragment the packets

## Slide 12: IPv6 extension headers - Fragmentation
Next Header
Identification
Reserved
Fragmentation Offset
Res
M
Fragmentation header
Notes: Next Header 8-bit selector. Identifies the initial header
type of the Fragmentable Part of the original
packet (defined below). Uses the same values as
the IPv4 Protocol field [RFC-1700 et seq.].
Reserved 8-bit reserved field. Initialized to zero for
transmission; ignored on reception.
Fragment Offset 13-bit unsigned integer. The offset, in 8-octet
units, of the data following this header,
relative to the start of the Fragmentable Part
of the original packet.
Res 2-bit reserved field. Initialized to zero for
transmission; ignored on reception.
M flag 1 = more fragments; 0 = last fragment.
Identification är en 32-bits räknare.
Alla delar går inte att fragmentera, IPv6 header + routing header + hop-by-hop header.
Paketen skickas som unfragmented parts + fragmentheader + fragment bit.

## Slide 13: IPv6 extension headers -Destination option
If we in the future want to extend the headers of IPv6, we could add more extensions headers
  This would however mean that we would use up more of the limited 255 codes
  It will also require that both the sender and the receiver understands the code

## Slide 14: IPv6 extension headers - Destination option
Next Header
Hdr Ext Len
Options

## Slide 15: IPv6 extension headers - Destination option
The destination decodes the field
If the destination can not handle the type it will send a “Unrecognized type” ICPMP message to the source
Today there are only two byte-padding destination option headers
Notes: Paddingen används för att fylla på till hela 64-bytes eller bytes boundaries

## Slide 16: IPv6 extension headers - Hop-by-Hop
All the other extension headers are processed by the final destination
The hop-by-hop header is processed by intermediary nodes
Hop-by-hop have the exact same coding s the destination option

## Slide 17: IPv6 extension headers - Hop-by-Hop
Next Header
Hdr Ext Len
Options

## Slide 18: IPv6 Flows
Flow:1843
Flow:220
Flow:3026
Notes: En flow är en ström av paket från samma källa till samma destination
  Med samma ”flow label”
Med samma extension headers
  Hop-by-Hop och routing
Detta är experimentellt och inte i ”riktig” användning
Varje flow identifieras och ”märks” av källan till trafiken
Varje flow måste vara unik
  En källa måste hålla isär att en nyligen tilldelad flow-lable inte har använts nyligen
Tanken är att flows kan användas för real-tidsapplikationer
  Flows kan då användas av tex ett RSVP för IPv6

## Slide 19: IPv6 Security
In IPv4, secure tunnels are built with IP-Sec
  IPv6 have similar functions as native
  IPv6 have an authentication header to verify the source
  Security to protect the data from external parties

## Slide 20: IPv6 security
Host
Host
Host
unreliable network
Host
Security gateway
VPN
VPN
Security gateway

## Slide 21: IPv6 Security - Authentication
Yet another extension header
Will be added after all the other extension headers, but before the payload.
The authentication header is specified in RFC2402
  Used to be part of the IPv6 specification
Extension hdrs
IPv6
Auth
Payload

## Slide 22: IPv6 Security - Authenctication
Next Header
Payload len
Reserved
Security Parameters Index
Authentication Data (Variable number of 32-bit words)
Sequence number field
Notes: Next header = nästa header typ
Payload len = längden på AH
--------------
2.4 Security Parameters Index (SPI)
The SPI is an arbitrary 32-bit value that, in combination with the
destination IP address and security protocol (AH), uniquely
identifies the Security Association for this datagram. The set of
SPI values in the range 1 through 255 are reserved by the Internet
Assigned Numbers Authority (IANA) for future use; a reserved SPI
value will not normally be assigned by IANA unless the use of the
assigned SPI value is specified in an RFC. It is ordinarily selected
by the destination system upon establishment of an SA (see the
Security Architecture document for more details).
The SPI value of zero (0) is reserved for local, implementation-
specific use and MUST NOT be sent on the wire. For example, a key
management implementation MAY use the zero SPI value to mean "No
Security Association Exists" during the period when the IPsec
implementation has requested that its key management entity establish
a new SA, but the SA has not yet been established.
Kent & Atkinson Standards Track [Page 4]
^L
RFC 2402 IP Authentication Header November 1998
2.5 Sequence Number
This unsigned 32-bit field contains a monotonically increasing
counter value (sequence number). It is mandatory and is always
present even if the receiver does not elect to enable the anti-replay
service for a specific SA. Processing of the Sequence Number field
is at the discretion of the receiver, i.e., the sender MUST always
transmit this field, but the receiver need not act upon it (see the
discussion of Sequence Number Verification in the "Inbound Packet
Processing" section below).
The sender's counter and the receiver's counter are initialized to 0
when an SA is established. (The first packet sent using a given SA
will have a Sequence Number of 1; see Section 3.3.2 for more details
on how the Sequence Number is generated.) If anti-replay is enabled
(the default), the transmitted Sequence Number must never be allowed
to cycle. Thus, the sender's counter and the receiver's counter MUST
be reset (by establishing a new SA and thus a new key) prior to the
transmission of the 2^32nd packet on an SA.
2.6 Authentication Data
This is a variable-length field that contains the Integrity Check
Value (ICV) for this packet. The field must be an integral multiple
of 32 bits in length. The details of the ICV computation are
described in Section 3.3.2 below. This field may include explicit
padding. This padding is included to ensure that the length of the
AH header is an integral multiple of 32 bits (IPv4) or 64 bits
(IPv6). All implementations MUST support such padding. Details of
how to compute the required padding length are provided below. The
authentication algorithm specification MUST specify the length of the
ICV and the comparison rules and processing steps for validation.

## Slide 23: Security - Encryption
Yet another extension header…
…the last one to be added, and the last “clear text” part of the header
What type of encryption depends on the crypto algorithm in use
  For more information see RFC2406
Extension hdrs
IPv6
Security
Encrypted payload

## Slide 24: IPv6 Quality of Service
For IPv4, DiffServ and IntServ have been defined. They make use of the TOS field
In IPv6 the “traffic class” field is created for the same functions
The standard is being worked out

## Slide 25: IPv6 Design and addressing
IPv6, 128-bits -> Much more text …
Three notations
  Most common is
  X:X:X:X:X:X:X:X
  Each X is the Hex representation of a 16-bit octet.
  Example
    FEDC:BA98:7654:3210:FEDC:BA98:7654:3210
    1080:0:0:0:8:800:200C:417A
    Note that you don’t need to write the leading zeros in each field

## Slide 26: IPv6 Design and addressing
  Due to the nature of the IPv6 addresses, many addresses will have only zero octets, leading to strings of zeros. In order to make the notation easier a group of zeros can be compressed as “::”
    Example
      1080:0:0:0:8:800:200C:417A
      Could be written as
      1080::8:800:200C:417A
      Note that only one group of zeroes can be written in this way 0:0:0:0:0:0:0:0
      Is written as
      ::

## Slide 27: IPv6 design and addressing
The address prefix and subnet works and is represented in the same ways as for IPv4
12AB:0000:0000:CD30:0000:0000:0000:0000/60
12AB::CD30:0:0:0:0/60
12AB:0:0:CD30::/60
  All are valid notations

## Slide 28: IPv6 Address types
IPv6 address types are determined by the prefix bits as
Address type Binary prefix IPv6 notation
------------ ------------- -------------
Unspecified 00...0 (128 bits) ::/128
Loopback 00...1 (128 bits) ::1/128
Multicast 11111111 FF00::/8
Link-local unicast 1111111010 FE80::/10
Site-local unicast 1111111011 FEC0::/10
Global unicast (everything else)

## Slide 29: IPv6 Link-local / Site-local
Link-Local
Not routed
Used at bootstrap
  For example a host could use it’s link-local address to send out DNS server discovery etc
Site-local
At the moment pretty controversial
Similar to RFC1918
Security - false saftey

## Slide 30: IPv6 addressing
IPv6 addresses are ”hierarchial”
  In other words, different blocks are handed out to different types of entities
001
TLA
NLA
SLA
3bits 13 bits 32 bits
16 bits 64 bits
Interface ID
TLA = Top Level Aggregate (/16)
NLA = Next Level Aggregate (/48)
SLA = Site Level Aggregate (/64)
Public Topology
Private Topology

## Slide 31: IPv6 Addressing
001
TLA
Res
NLA
SLA
Interface ID
3 13 8 24 16 64

## Slide 32: IPv6 Addressing - 6bone
In order to “practice” transition a early IPv6 network was created - 6bone
Still mostly tunnels are built to extend and connect to the 6bone
  Partly due to the ease of getting addresses
  However, the 6bone can also be seen as a blocking factor to create further native deployment

## Slide 33: IPv6 Addressing - 6bone
To get away from a tunnled infrastructure built around 6bone
  The 6bone addresses will be recalled
  The current users of the 6bone will have to turn to their ISP and ask for IPv6 addresses
  Hopefully this will trigger interest from more ISPs to apply for IPv6 address space and starting building their native IPv6 service

## Slide 34: IPv6 Addressing - Production addresses
001
TLA
NLA
SLA
Interface ID
3 13 13 6 13 16 64
sTLA
Res
TLA assignments
  2000::/16 Reserved
  2001::/16 sub-TLA assignments
  2002::/16 6to4
sTLA i 2001::/16
  2001:0000::/29 IANA
  2001:0200::/29 APNIC
  2001:0400::/29 ARIN
  2001:0600::/29 RIPE-NCC

## Slide 35: IPv6 Unicast addresses
For IPv6 Unicast addresses, the last 64-bits are defined by the interface
  EUI64 coded, but with “modifed” EUI64
  Inverted ’g’ bit
0 0 0 1 1 2
|0 7 8 5 6 3|
+----+----+----+----+----+----+
|cccc|ccug|cccc|cccc|cccc|cccc|
+----+----+----+----+----+----+
    Marks globally or locally unique EUI64 address
  True for all unicast addresses except for host that have a prefix of 000

## Slide 36: Discussions on EUI64 coding
A EUI64 address is unique per interface and therefore per host
  Some claims that this is a threat to personal integrity
  On the other side, a IP address itself if pretty revealing
  EUI64 addresses or actually interface addresses are normally changeable

## Slide 37: IPv6 special addresses
The unspecified address
  Equivalent to the default route in IPv4, but also a address
  0:0:0:0:0:0:0:0/128
  Used as source address by nodes before they have a real address (autodiscovery)
Loopback address
  0:0:0:0:0:0:0:1/128
  Same function as for IPv4

## Slide 38: IPv6 Unicast addresses
| n bits | m bits | 128-n-m bits |
+------------------------+-----------+----------------------------+
| global routing prefix | subnet ID | interface ID |
+------------------------+-----------+----------------------------+

## Slide 39: IPv6 Addresses with IPv4
To ease the transition between IPv4 and IPv6, a tunneling technology have been defied where Ipv6 packets are sent in a IPv4 tunnel
The IPv6 packets will have addresses that starts with a prefix of 000
  Instead of having a EUI64 id as the last 64-bits, the nodes IPv4 address will be coded

## Slide 40: IPv6 Anycast addresses
A anycast address is a address that is defined on several interfaces
Through routing the “closest interface” will be chosen

## Slide 41: IPv6 Anycast adress
Subnetprefix is the same as for the rest of the subnet
Subnetprefix
Anycast id
n bits
121-n bits
7 bits
Notes: The construction of a reserved subnet anycast address depends on the
type of IPv6 addresses used within the subnet, as indicated by the
format prefix in the addresses. In particular, for IPv6 address
types required to have 64-bit interface identifiers in EUI-64 format,
the universal/local bit MUST be set to 0 (local) in all reserved
subnet anycast addresses, to indicate that the interface identifier
in the address is not globally unique. IPv6 addresses of this type
are currently specified to be those having format prefixes 001
through 111, except for Multicast Addresses (1111 1111) [3].
Specifically, for IPv6 address types required to have to have 64-bit
interface identifiers in EUI-64 format, these reserved subnet anycast
addresses are constructed as follows:
| 64 bits | 57 bits | 7 bits |
+---------------------------------+------------------+------------+
| subnet prefix | 1111110111...111 | anycast ID |
+---------------------------------+------------------+------------+
| interface identifier field |
For other IPv6 address types (that is, with format prefixes other
than those listed above), the interface identifier is not in EUI-64
format and may be other than 64 bits in length; these reserved subnet
anycast addresses for such address types are constructed as follows:
Johnson & Deering Standards Track [Page 2]
^L
RFC 2526 Reserved IPv6 Subnet Anycast Addresses March 1999
| n bits | 121-n bits | 7 bits |
+---------------------------------+------------------+------------+
| subnet prefix | 1111111...111111 | anycast ID |
+---------------------------------+------------------+------------+
| interface identifier field |