## Slide 1: Transition from IPv4 till IPv6

## Slide 2: Dual Stack - The easy way
IPv4 API /
Stack
IPv6 API /
Stack
Link layer
Transport layer
Application layer

## Slide 3: Dual stack
Advantages
  Easy to remove IPv4 once all applications support IPv6 and transport have proved stable
  Easy network design - it’s either IPv4 or IPv6
  No DNS problems etc
Disadvantages
  Assumes IPv6 end-to-end connectivity

## Slide 4: 6to4
In 6to4 a IPv4 address is mapped to a IPv4 address
  Predefined prefixet is 2002::/16
001
TLA
IPv4 Adress
SLA
Interface ID
3 13 32 16 64

## Slide 5: 6to4
IPv6
IPv4
IPv6
2002:192.168.1.1.0:1:2:3
S-IP: 2002:192.168.1.1.0:1:2:3
D-IP: 2002:10.0.0.1:0:1:2:3
192.168.1.1
10.0.0.1
S-IP: 192.168.1.1
D-IP: 10.0.0.1
S-IP: 2002:192.168.1.1:0:1:2:3
D-IP: 2002:10.0.0.1:0:1:2:3
S-IP: 2002:192.168.1.1:0:1:2:3
D-IP: 2002:10.0.0.1:0:1:2:3
2002:10:0:0:1:0:1:2:3

## Slide 6: Assignment of IPv4 global addresses to IPv6 Hosts (AIIH)
IPv6
IPv4
IPv6
::192.1.4.5
::C001:0405
0:0:0:0:0:0:C001:0405

## Slide 7: Tunnels
IPv6
IPv4
IPv6
IPv6
IPv6

## Slide 8: Tunnels
Tunnels can be static
  I.e Permanently configured
Dynamic
  ”Dial-on-demand”
  Tunnels will be brougt up when needed
Tunnels can be between
  Host-Host
  Host-Router
  Router-Router

## Slide 9: Tunnels exampel - Router-to-Router
ipv6 unicast-routing
interface Tunnel10
description TO KQ FI
no ip address
ipv6 enable
ipv6 address 2001:670:87:3001::1/126
tunnel source 195.43.225.65
tunnel destination 193.94.250.58
tunnel mode ipv6ip
tunnel checksum
ipv6 route ::/0 Tunnel10

## Slide 10: Tunnels exampel - Router-to-host
The router side looks the same…
Host (FreeBSD) :
$ ifconfig gif0 inet 194.112.11.163 195.43.225.65
$ ifconfig gif0 inet6 2001:670:87:3001::6 prefixlen 12
$ route add -inet6 2001:670:87:3001::4 -prefixlen 126 -interface gif0
$ route add -inet6 default 2001:670:87:3001::5

## Slide 11: Tunnels exampel - Router-to-Host
$ ifconfig gif0
gif0: flags=8010<POINTOPOINT,MULTICAST> mtu 1280
inet 194.112.11.163 --> 195.43.225.65 netmask 0xffffff00
inet6 2001:670:87:3001::6 --> :: prefixlen 12

## Slide 12: Other transition techniques
SIIT
  Uses ICMP to translate IPv4 - IPv6 through gateways
NAT-PT
  Traditional NAT/PT but instead of doing RFC1918 translation, IPv4/IPv6 is translated
ALG / Application Layer Gateway
  In principle a proxy per service ; Web, Mail etc.

## Slide 13: How do I do a native configuraiton?
interface FastEthernet0
ip address 195.43.225.65 255.255.255.224
ip pim sparse-mode
speed 10
half-duplex
ipv6 enable
ipv6 address 2001:670:87:1::/64
ipv6 nd prefix-advertisement 2001:670:87:1::/64 300 300 autoconfig
no cdp enable