## Slide 1: Routing

## Slide 2: IPv6 routing
In principle the same routing protocols and mechanims as for IPv4
  RIPng, IS-IS and OSPF for IGP
  BGP for EGP

## Slide 3: IPv6 routing - IGP
OSPF
  Modfied for the longer IPv6 addresses
  RFC2740
ISIS
  A draft existis for handling IPv6
  In principle two new TLVs
RIPng
  The first IGP for IPv6

## Slide 4: IPv6 routing - EGP
BGP-MP
  Also handeles IPv6 preficxes
  Behaves as ”ordinary” BGP
Multi6
  The problem with business as usual is that nothing is done to stop the growth of the default free zone
  The IETF muti6 WG exists to investigate alternative ways of doing multihoming
    Host or router based? Or both?

## Slide 5: IPv6 routing - BGP example
router bgp 3220
no synchronization
bgp log-neighbor-changes
neighbor ipv6-peer peer-group
no neighbor ipv6-peer activate
neighbor 2001:670:87:3001:: remote-as 790
no neighbor 2001:670:87:3001:: activate
neighbor 2001:670:87:3001::10 remote-as 1259
no neighbor 2001:670:87:3001::10 activate
!
address-family ipv6
neighbor ipv6-peer activate
neighbor ipv6-peer route-map ipv6-peer-in in
neighbor ipv6-peer route-map ipv6-peer-out out
neighbor 2001:670:87:3001:: peer-group ipv6-peer
neighbor 2001:670:87:3001::10 peer-group ipv6-peer
network 2001:670:87::/48
exit-address-family